AGENCY REQUEST

JUNE 2011

#### AGENCY: 	Department of Health Services

PROJECT:	Storage Bunker Repairs, Project #11E2D

LOCATION:	Mendota Mental Health Institute, Madison, Dane County

PROJECT REQUEST:

Provide authority to

- Construct a project to repair the Heating Plant storage bunker at the Mendota Mental Heath Institute at an estimated total project cost of $556,300 General Fund Supported Borrowing – Facilities Repair and Renovation; and

- Transfer all approved GFSB All Agency Allocations to the DHS Infrastructure Maintenance appropriation [Z460].

Project Description / JUSTIFICATION:

In 1954 the current heating plant was constructed and used the coal storage bunkers built with the original heating plant, circa 1909. In 1963 substantial changes were made to the plant; the bunkers’ fill chutes were closed. The bunkers were then opened to the basement of the new plant and, since that time, have been used to store materials, supplies and equipment needed to operate and maintain the plant. Also in the early 1960s restoration work was completed on the eastern end of the structure. With the exception of the upper portion of the west wall and the roof, the 163’ long by 63’ wide structure is underground.

Currently, the storage bunker shows signs of severe deterioration. The large concrete beams supporting the roof, as well as the roof, walls and structural columns show cracking and spalling. In some areas spalling has exposed reinforcing steel. Leakage occurs at some of the infill areas. The west end wall shows large vertical and horizontal cracks, which extend through the wall. The exterior surface of the wall shows extensive spalling. The local fire department has declared the structure unsafe for occupancy and will not enter in case of an emergency. A localized area of similar deterioration exists in the Lorenz Hall loading dock.

A full structural analysis of the Heating Plant storage bunkers and the Lorenz Hall loading dock was conducted in 2010. The analysis mapped areas of deterioration, recommended possible repairs and developed associated cost estimates. The potential of closing the storage bunkers and providing storage elsewhere was also reviewed in the analysis, but it was determined that portions of the bunker repair would need to be completed prior to the bunker abandonment. For this reason, this option proves economically unacceptable.

This project will perform major restoration to the storage bunkers at the Heating Plant based on the 2010 structural analysis report. Structural repairs will be done to the deck, walls and columns, and the roof deck will be waterproofed. Similar, but limited, repairs will be preformed at the Lorenz Hall loading dock.

DHS Contact: Ed Neckar, (608) 267-4594, edwin.neckar@wisconsin.gov

BUDGET & SCHEDULE:

11E2D – Storage Bunker Repairs - $556,300

Mendota Mental Health Institute

| Budget | Cost | Schedule | Date |
| --- | --- | --- | --- |
| Construction | $406,500 | Commission Approval | June 2011 |
| Contingency | $69,400 | A/E Selection | July 2011 |
| A/E Fee | $56,100 | Bidding | March 2012 |
| DSF Mgmt/Fees | $18,700 | Start Construction | May 2012 |
|  | $550,700 | Final Completion | January 2013 |

PREVIOUS ACTION: None